## Slide 1: Session 1 – ENC Conversion (sub)WG meeting Oct 7th 2020
Agenda
  Welcome
  TORs
  Where are we?
  Workplan
  How do we work?
  Next Meetings, Actions
Guidance for TORs:
  Develop rules for HOs on addressing ENC inconsistencies in data before conversion. Engage with KHOA on lessons learn from their trial.
  Produce encoding guidance for HOs that will assist the automation of the conversion process. We must have some real world examples that have been proven to reduce manual processing
  Encoding must be tested to ensure it does not adversely affect existing ENC display in ECDIS.

## Slide 2: Where are we?
Tools
  NIWC viewer works with FC and PC
  Caris composer contains mapping engine, tested for S-64 unencrypted test datasets
  Github for this subWG (https://github.com/iic-tech/enc_conv)
Schemas
  IHO Schema in progress but good enough to make test datasets. Missing a number of relationships. PC allows for initial creation of S-164 screenshots
Test Data
  Initial (Phase 1)S-64 test datasets available for review/update (https://github.com/iic-tech/S-164). Also contains text dumps of contents.
  No systematic / exhaustive test datasets (yet)
  KHOA test datasets also available (earlier release)
  Others available (Null Island, Edge Cases) – not in github yet.
Guidance
  Documentation from IHO (Jeff), Spreadsheet of modifications to features, attributes, primitives etc…
  FC contains existing acronyms ( good for identifying dictionary conversions)
  Report (IIC) outlines methodology but no tools currently exist to support
  Initial edge case list (JP) in github
  Testing and development in progress
  No recommended migration methodology

## Slide 3: Types of Conversion
Simple dictionary conversion
  Where feature and attribute bindings don’t change and are just re-labelled
  Mapping from feature->feature and attribute->attribute
  80% of content (?) of current ENCs
Edge Cases
  Use INFORM to control what is being defined/populated
  Geometric primitives which have changed/dropped
  Changes to enumerations / meanings
  New/Dropped features
  Relationships
Special considerations
  Hazards / Alerts features
  Where portrayal may be different
  Where manual intervention may be required
  UPDATES